## Slide 1
SANKHYA
An indigenous optimization solver: LP, MILP, convex QP and NLP, written from the textbooks in C++20, with a GPU first-order engine and an independent checker on every answer.
Smart India Hackathon 2026 - problem statement SIH26119 - Mangalore Refinery and Petrochemicals Limited
Every number in this deck is computed from a CSV in bench/results/ on main, named on the slide, by tools/make_deck.py; the same CSVs produce docs/REPORT.pdf and docs/BENCHMARKS.md. github.com/thegoodengineers/SANKHYA - sankhya-solver.vercel.app

## Slide 2
The problem: a refinery plans in LPs, MILPs and QPs, on someone else's solver
Source: the problem statement SIH26119 as issued; docs/PS26119_COVERAGE.md
Which crudes to buy, how hard to run each unit, how to blend to specification: the weekly plan is a linear program, the unit on/off and minimum-run decisions make it mixed-integer, and price-dependent blending makes it quadratic.
The problem statement asks for an indigenous, GPU-accelerated solver as a sovereign alternative to CPLEX and Xpress: LP, MILP, QP, presolve, cuts, sensitivity, multi-core and GPU, benchmarked on Netlib, MIPLIB and Mittelmann, and not built on any existing solver.
SANKHYA is that solver, from a blank repository on 25 August 2026. What follows is what is on main today, with the file behind each number.
What a judge can do in five minutes
1. pip install the wheel from the release, or unpack an archive: no compiler.
2. sankhya solve demo/crude_blend.mps --write-sol blend.sol
3. python tools/verify_solution.py demo/crude_blend.mps blend.sol: a checker that shares no code with the solver re-derives the answer.
4. demo/finale.sh: one refinery MILP solved, proved in exact arithmetic, priced, broken and repaired, re-planned from yesterday's basis.
5. Open docs/REPORT.pdf: every claim with its CSV and commit.

## Slide 3
Architecture: one Model, one solve(), several engines, one checker outside
Source: docs/ARCHITECTURE.md; docs/PROVENANCE.md section 3 for the paper above each file
Read
- MPS and LP readers (src/io)
- gz inputs
- Model: the frozen interface every reader produces and every engine consumes
Presolve
- reductions with a postsolve stack (src/presolve)
- scaling by powers of two, geometric prescaling on retry
- convexity test for a QP: LDL^T, a negative pivot is the certificate
Solve
- revised primal and dual simplex: Markowitz LU, Forrest-Tomlin, dual steepest edge (src/simplex, src/la)
- restarted PDHG on the CPU and, through CUDA, on the card (src/pdhg, src/gpu)
- Mehrotra interior point, sparse LDL^T, crossover (src/ipm)
- proximal interior point for convex QP (src/qp)
- branch and cut: cuts, heuristics, SOS, certificates (src/mip)
- local NLP and convex MINLP (src/nlp)
Report
- Solution: objective, point, duals, ranging, basis, certificate
- C API, CLI, ctypes Python bindings, PuLP / Pyomo / CVXPY adapters
- tools/verify_solution.py and tools/verify_certificate.py: read only the files, never link the solver

## Slide 4
Correctness evidence: an answer is reported only after a separate program agrees
Source: bench/results/netlib-full-945cb4f.csv, bench/results/netlib-infeasible-5a39fb2.csv, bench/results/certified-gap-netlib-full-945cb4f.csv, bench/results/exact-sensitivity-60455ce.csv, bench/results/stress-d32b3847.csv
what is checked | result | CSV | commit
Netlib LP, full set: accepted by the independent verifier | 94 of 94 | bench/results/netlib-full-945cb4f.csv | 945cb4f
Netlib LP: within 1e-6 of Koch's exact rational optimum and verified | 94 of 94 | bench/results/netlib-full-945cb4f.csv | 945cb4f
Netlib infeasible LPs: verdict with a Farkas certificate the verifier accepts | 28 of 29 | bench/results/netlib-infeasible-5a39fb2.csv | 5a39fb2
Optimal Netlib answers with a rigorous (Neumaier-Shcherbina) bound within 1e-6 | 91 of 94 | bench/results/certified-gap-netlib-full-945cb4f.csv | 945cb4f
Duals, reduced costs and ranges re-derived in rational arithmetic (LPs done) | 69 of 96; 4,479 of 431,730 values corrected | bench/results/exact-sensitivity-60455ce.csv | 60455ce
Stress set of badly scaled and adversarial LPs: correct / wrong / declined | 111 / 0 / 15 of 126 | bench/results/stress-d32b3847.csv | d32b3847
HiGHS 1.15.1 on its defaults, same set: correct / wrong / failed | 29 / 90 / 7 of 126 | bench/results/stress-d32b3847.csv | d32b3847
tools/verify_solution.py reads the model file and the written .sol file with its own parsers and never links the C++. A verdict of infeasible or unbounded arrives with a certificate it checks the same way; a MILP's proof is a VIPR certificate checked in exact arithmetic (tools/verify_certificate.py).

## Slide 5
Head-to-head on LP: HiGHS, SCIP, CBC/Clp and GLPK, same machine, one thread
Source: bench/results/head-to-head-netlib-5e490ef.csv (5e490ef); bench/results/head-to-head-kennington-1860864.csv (1860864); method in docs/BENCHMARKS.md section 4a
Netlib LP, 92 instances, 120 s limit: shifted geometric mean time, shift 10 s
SANKHYA
0.575 s
HiGHS
0.163 s
SCIP
0.398 s
CBC/Clp
1.355 s
GLPK
0.486 s
Kennington LP, 16 instances, 120 s limit
SANKHYA
9.43 s
HiGHS
1.855 s
SCIP
10.899 s
CBC/Clp
0.795 s
GLPK
7.345 s
Against HiGHS instance by instance: Netlib faster on 3, tie on 72, slower on 17 of 92; Kennington faster on 3, tie on 2, slower on 11 of 16 (a tie is within 10%).
The same verifier checks every rival's answer; on Netlib it rejected 5 rival answers. A run that is not optimal, at the published optimum and verified is charged the full time limit (Mittelmann's convention).
SANKHYA is not the fastest LP solver here and this deck does not say it is: it is the one whose every answer, and every rival's, went through the same independent check.

## Slide 6
Convex QP and MILP: where the checker changes the ranking
Source: bench/results/head-to-head-maros-meszaros-1860864.csv (1860864); bench/results/maros-meszaros-cad720c.csv (cad720c); bench/results/miplib-ad57c03.csv (ad57c03)
Maros-Meszaros convex QP, 138 instances, 60 s limit, head-to-head
solver | runs | solved | matched | verified | SGM time, shift 10 s
SANKHYA | 138 | 107 | 106 | 107 | 6.437 s
HiGHS | 138 | 105 | 99 | 32 | 35.781 s
SCIP | 138 | 78 | 76 | 53 | 27.436 s
CBC/Clp | 138 | 127 | 113 | 62 | 20.974 s
GLPK | 138 | unsupported | - | - | -
A rival's optimal status is not taken on trust either: the verifier rejected 163 rival QP answers in this run, and only verified runs count for time. Against HiGHS instance by instance: faster on 82, tie on 22, slower on 5 of 109.
Alone, on the laptop: 117 of 138 at the published objective, 0 optimal answers rejected (bench/results/maros-meszaros-cad720c.csv).
14 of 30
MIPLIB 2017 easy set at the published optimum, 11 of 30 proved optimal inside the limit (bench/results/miplib-ad57c03.csv)
64 of 70
Hock-Schittkowski NLP at the published objective, 70 accepted by the checker (bench/results/nlp-hs-ad57c03.csv)
14 of 17
convex MINLPLib at the published objective, 16 accepted (bench/results/nlp-minlplib-ad57c03.csv)

## Slide 7
GPU: the first-order engine on an NVIDIA A100-SXM4-40GB, against the faster CPU arm
Source: bench/results/gpu-real-a100-fdd1f35.csv (fdd1f35); docs/BENCHMARKS.md section 1g.3; the L4 run beside it in gpu-real-l4-58a8374.csv
model | rows | tolerance | card | faster CPU arm | card status | speed-up
brazil3 | 14,646 | 1e-04 | 5.2 s | 38.7 s (cpu-16t) | feasible | 7.50x
brazil3 | 14,646 | 1e-08 | 10.5 s | 91.8 s (cpu-16t) | feasible | 8.72x
chromaticindex1024-7 | 67,583 | 1e-04 | 0.4 s | 0.9 s (cpu-16t) | feasible | 2.02x
chromaticindex1024-7 | 67,583 | 1e-08 | 0.5 s | 0.9 s (cpu-16t) | feasible | 1.65x
refinery_year | 779,640 | 1e-04 | 300.5 s | 300.5 s (cpu-1t) | time_limit | 1.00x
refinery_year | 779,640 | 1e-08 | 300.5 s | 300.5 s (cpu-1t) | time_limit | 1.00x
1.00x to 8.72x over 6 model-tolerance cells, 2 of them ending at the time limit on every arm. The card wins where the model is large and loses below about 10,000 rows, where launching kernels costs more than the arithmetic; the readme and section 1g name the losses.
The CUDA port is the same restarted PDHG: cuSPARSE products, CUB reductions in a fixed order (deterministic), the iteration loop captured as a CUDA graph, convergence evaluated on the device. A CPU build with no card warns and solves on the CPU; the CUDA archive is compiled in CI without a card.
HiGHS on the same host is still faster on brazil3 than the card at 1e-8 (readme, section 1g.3): the GPU story is a real speed-up of our own engine, not a claim over the field.

## Slide 8
Scale: a million rows on the CPU, and where large LPs stop today
Source: bench/results/million-cpu-b561fba.csv (b561fba); bench/results/mittelmann-72123ff.csv (72123ff); bench/results/kennington-full-9463fd7.csv (9463fd7)
2 of 9
engine runs at a million rows optimal and verified: transport 1,000,000 rows by pdhg in 119 s; refinery 1,007,400 rows by pdhg in 2,336 s
16 of 16
Kennington LPs matched to the published optimum and verified (bench/results/kennington-full-9463fd7.csv)
5 of 12
Mittelmann LPs solved and verified inside the limit (bench/results/mittelmann-72123ff.csv). This is where the solver stops: the rest end on the interior point's ordering budget or the time limit, named row by row in docs/BENCHMARKS.md section 1d.
Large LPs are routed by the normal-equations bound and the dual's work: the simplex below, the interior point above, PDHG for what neither factors. Time limits reach inside the factorization, so a run stops on time, not when the factor happens to finish.

## Slide 9
The refinery demo: one MILP solved, proved, priced, broken, repaired, re-planned
Source: docs/FINALE.md; bench/results/scenarios-de0f393a.csv (de0f393a); bench/results/million-cpu-b561fba.csv (b561fba); model from bench/case_studies/refinery/generator.py
demo/finale.sh, eight steps, each one printed line and its time, the script stopping at the first check that fails:
1. solve the small refinery MILP with a VIPR certificate (on the card when there is one)
2. prove it: the certificate in exact rational arithmetic, the plan by the verifier
3. plan: the binding limits and their shadow prices, each re-solved one unit looser, so a degenerate price is not mistaken for the value of the next unit
4. repair: a delivery commitment raised until the plant cannot meet it; the Farkas proof checked, the smallest repair found
5. bundle: an evidence bundle made and replayed, the proof checked again
6. prices: twenty crude price sets through sankhya scenarios
7. replan: today's prices and demands, cold and from yesterday's basis (--warm-start)
8. units: a minimum run rate as semi-continuous columns, branched natively and through the binary reformulation, the two answers verified and equal
Synthetic data from a fixed seed: no real industrial model has been run (a stated limit).
1130 of 1130
scenarios verified, each re-solved from the base basis by the dual simplex and checked against its own model, agreeing with its single solve (bench/results/scenarios-de0f393a.csv)
1,007,400 rows
the refinery family at a million rows, optimal and verified on the CPU (transport 1,000,000 rows by pdhg in 119 s; refinery 1,007,400 rows by pdhg in 2,336 s)

## Slide 10
Packaging: no compiler needed, checked on a fresh machine by CI
Source: .github/workflows/release.yml; docs/PROVENANCE.md section 2b; the v1.0.0-rc2 release
Release archives: Linux x86-64 CPU and CUDA (runtime linked in), Windows x64 CPU, each unpacked and run on a runner with no compiler before the draft release exists.
Python wheels: ctypes over the C API, one wheel per platform for CPython 3.9 to 3.13, each installed into a clean venv of every version, the demo solved and verified there.
Container image on ghcr.io: the CUDA build, the verifier and the demo models.
C API (include/sankhya/sankhya.h), CLI (solve, diagnose, scenarios, engines, info), Python bindings, and adapters that make SANKHYA the solver under PuLP, Pyomo and CVXPY models.
Every archive's MANIFEST.txt records the commit, compiler and libraries; CI fails the packaging if any of them is an optimization solver.
pip install https://github.com/thegoodengineers/SANKHYA/releases/download/v1.0.0-rc2/sankhya-1.0.0-py3-none-manylinux_2_35_x86_64.whl
python -c "import sankhya; print(sankhya.Model.read('demo/crude_blend.mps').solve().objective)"
sankhya solve demo/crude_blend.mps --write-sol blend.sol
python tools/verify_solution.py demo/crude_blend.mps blend.sol

## Slide 11
Honest limits: what the numbers do not say
Source: bench/results/head-to-head-netlib-5e490ef.csv; bench/results/head-to-head-kennington-1860864.csv; bench/results/mittelmann-72123ff.csv; bench/results/miplib-ad57c03.csv; bench/results/stress-d32b3847.csv; bench/results/certified-gap-netlib-full-945cb4f.csv; docs/NEGATIVE-RESULTS.md
Speed against HiGHS: Netlib SGM 0.575 s against 0.163 s; Kennington 9.430 s against 1.855 s, slower on 11 of 16 instances.
Large LPs: Mittelmann 5 of 12 inside the limit.
MILP proofs: 11 of 30 MIPLIB 2017 instances proved, 14 at the published optimum.
Declined instances: stress set 15 of 126 declined (0 wrong); Maros-Meszaros 119 of 138 optimal; safe bounds, 2 of 94 optimal answers with no finite bound, and they say so.
The GPU: 1.00x at the low end of the 6 cells, a loss below about 10,000 rows, 2 cells at the time limit; HiGHS on the same host beats the card on brazil3 at 1e-8.
No real industrial model: every refinery number is from a generated model with a fixed seed.
What was built and then demoted, left opt-in or withdrawn, with the number that did it, is kept by name in docs/NEGATIVE-RESULTS.md.

## Slide 12
Provenance: not built on any solver, and CI proves it on every build
Source: docs/PROVENANCE.md; docs/sbom.spdx.json; .github/workflows/ci.yml, job provenance
The red line: no source from CBC, Clp, HiGHS, SCIP, SoPlex, GLPK, lp_solve, OSQP, PDLP, cuPDLP, OR-Tools, Gurobi, CPLEX or Xpress was copied, vendored, linked or read: not a simplex, not a cut, not an MPS reader.
Every algorithm names the paper or textbook it was written from, above the code and in the citation table (Dantzig, Chvatal, Maros, Koberstein, Forrest-Tomlin, Harris, Markowitz, Chambolle-Pock, Applegate et al., Mehrotra, Neumaier-Shcherbina, ...).
Dependencies are the non-solver kind, each with its licence and one line on why it is not a solver: fmt, CLI11, nlohmann/json, zlib, GoogleTest, cuSPARSE, CUB, OpenMP; HiGHS, SCIP, CBC and GLPK exist only as separate processes in the benchmark harness.
CI prints the full link line and ldd of the binary and fails if a solver library ever appears; the SPDX SBOM is committed, not only produced; every path the citation table names must exist.
Judgement calls, where a line could be argued, are logged with their reasoning in the same document rather than decided silently.

## Slide 13
Team: the good engineers
Source: sankhya-solver.vercel.app/team; git log
Bhumika Gurav
team lead
Deekshith K
engineer
Anjankumar L N
engineer
Abhijeet Sharma
engineer
Ayush V Upadhye
engineer
Chirag Honnyal
engineer
Rules the repository enforces on us: no number without a CSV, correct over fast, the paper cited above the code, and what is missing said with the number.

## Slide 14
Where to look
Source: README.md; docs/REPORT.pdf; docs/BENCHMARKS.md; docs/VIDEO.md; sankhya-solver.vercel.app
github.com/thegoodengineers/SANKHYA: the source, the CSVs, the CI runs.
docs/REPORT.pdf: this evidence as one document with a 25-question jury Q&A, every answer naming its file.
docs/BENCHMARKS.md: every suite, every failure named, generated from the CSVs.
docs/VIDEO.md: the four-minute walkthrough, command by command.
sankhya-solver.vercel.app: the problem, the solver, the evidence, how to run it, the team.
Clone it, build it, run scripts/reproduce.sh, and report any number that does not reproduce.